## Slide 1: Light Painting
ME547 – Final Project
Atakan Efe Kanman
Ahmed Syed
Jasdeep Dhillon

## Slide 2: Problem Definition
Light painting
Capturing light trails using long exposure photography
Drawing images in air
Requires some method of moving light source
  Hard to do by hand (cannot see trail with eyes)

## Slide 3: Objective
Create and communicate a desired path to the robot
Recreate path with robot’s end effector

## Slide 4: Main Tasks
Receive path from user
Map path to robot’s workspace
Send path waypoints to robot
Capture long exposure photo of movement

## Slide 5: Flow Diagram
Detect coloured object
Find center in pixels
Store (x,y) in array as % of picture dimension
Complete?
Write array to text file
Read text file
Map coordinate to robot workspace
Get robot parameters through inverse kinematics
End of file?
Send command to robot
Path Generation
Path Recreation
YES
NO
NO
Start
End
YES

## Slide 6: Path Generation
Computer vision based detection
  OpenCV
  Personal computer
Main Steps:
  Capture video frame from webcam
  Detect specific colour and mask image
  Find center of masked object
  Draw line from previous point to new point

## Slide 7: Path Generation - continued
Detecting object
Find all pixels with desired HSV values
  Hue: 147-179 (red)
  Saturation/Value: Depend on lighting

## Slide 8: Detecting Red Mitt
Video here

## Slide 9: Path Generation - continued
Find center of masked image
  Draw line from current center to previous center
Store position as a percentage of picture dimensions
  X = x / width
  Y = y/ height
(0,0)
(x,y)

## Slide 10: Tracking Center
Video here

## Slide 11: Mapping Points to Robot Workspace
The origin of the robot space and captured image do not align
  Image: top left
  Robot: bottom right
X = maxX – (x)(x-range); Z = maxZ – (z)(z-range);
z
(0,0)
(640,480)
x
Image
Workspace
(max X, max Z)

## Slide 12: DH Table
i | ai | αi | di | θi
1 | 0 | -90 | 0 | θ1
2 | 260 | 180 | 0 | 
3 | 290.07 | 0 | 0 | 
4 | 0 | 90 | 0 | θ4
5 | 0 | 0 | 73 | θ5
i | ai | αi | di | θi
1 | 0 | -90 | 0 | θ1
2 | 260 | 180 | 0 | 
3 | 290.07 | 0 | 0 | 
4 | 0 | 90 | 0 | θ4
5 | 0 | 0 | 73 | θ5

## Slide 13: Inverse Kinematics
Purpose: Move light source to points along the path drawn by the user
xc = 480 - (x * 240)
yc = 0
zc = 250 - (z * 180)

## Slide 14: Inverse Kinematic Results
θ1 = 0
θ4 = 0
θ5 = 0

## Slide 15: Testing
Attach 3mm LED to end effector
Take long exposure photo with smartphone
  Max exposure time of 10 seconds

## Slide 16
Videos here

## Slide 17: Results

## Slide 20: Conclusion
Completed both objectives
  Able to track object and define a path
  Able to follow path to recreate image
Resulting images were skewed
Did not follow path perfectly
Improvements:
Increase number of waypoints for smoother curves
Better camera with longer exposure time
Allow larger workspace to reduce scaling